## Slide 1: LEAN Principles
Total Productive Maintenance (TPM)
Operational Equipment Effectiveness (OEE)

## Slide 2: Goal of LEAN
Making your shop more efficient
By making equipment run more often not just faster.
You can make more product by making better use of your time than you can by making things go faster. It’s the Tortoise vs the Hare.

## Slide 3: Todays Shop Challenges
Labor is getting harder to find and more expensive.
Training good people is time consuming.
New Equipment is expensive.
Floor space is precious and short in supply.
We all need to utilize what we have better vs getting more machines and hiring more people to run it.

## Slide 4: Session 1: Overview of TPM

## Slide 5: What is TPM?
Total Productive Maintenance (TPM) is a method to achieve maximum equipment effectiveness through employee involvement
Management + Operators + Maintenance
Overview of TPM

## Slide 6: Machine failures have many hidden causes
Overview of TPM
$$$$$$Failure$$$$$
Loosening
Contamination
Corrosion
Leaks
Flaws
Deformation
Vibration
Cracks
Backlash
Improper
Temperature
Wear
Less
Visible
Visible
Failure is what we see but is only the tip of the iceberg
Minor machine defects are generally unnoticed but are the cause of almost all machine failures
Failures are more expensive than maintenance

## Slide 7: Failures Mean $$$
Lost productive time $$$
Production of defects $$$
Leads to shortages down stream in the manufacturing process. $$$
Employee expense from inflicted downtime.
Late delivery or overtime costs $$$
Overview of TPM

## Slide 8: TPM is a Paradigm Shift
Overview of TPM
Old Attitude
TPM Attitude
I use
I maintain &
I fix
We maintain
Maintenance
Operator
Maintenance
Operator

## Slide 9: TPM Approach
Preventing breakdowns
Modifying equipment to prevent breakdowns and make maintenance easier and faster.
Being prepared for common equipment failures.
Have the parts on hand and the skills to make repairs as needed.
Overview of TPM

## Slide 10: Small Group Activities: Problem-solving Process
Define the Problem
Collect Data
Identify the
Root Causes
Implement
Countermeasures
Evaluate &
Follow Up
A
B
D
E
C
F
Key TPM Tools

## Slide 11: Equipment Loss Analysis & OEE
Make it run more not faster

## Slide 12: Introduction to OEE
OEE (Overall Equipment Effectiveness) is a metric that identifies the percentage of planned production time that is truly productive
How to understand OEE score?
  An OEE score of 100% is perfect production
  An OEE score of 85% is world class for discrete manufacturers
  An OEE score of 60% is fairly typical for discrete manufacturers
  An OEE score of 40% or less is not uncommon for manufacturers without TPM and/or lean programs
What is your organization’s OEE score?
Equipment Loss Analysis & OEE

## Slide 13: Typical OEE Measurement
Availability X Performance X Quality

## Slide 14: Typical OEE Measurement
Availability = Actual Run Time
= 0.76 76% uptime

## Slide 15: Typical OEE Measurement
Performance
Performance = = 0.468
= 47%
This is where the most losses are found. Changeovers and idle times between cycles of making a part etc etc….

## Slide 16: Typical OEE Measurement
Quality = 0.933 93%

## Slide 17: Typical OEE Measurement
Availability X Performance X Quality
Example Model 0.76 0.468 X 0.933= 0.33 33%
After improving machine process
0.76 0.86 X 0.933= 0.609 61%

## Slide 18: Typical OEE Measurement
Improve machine effectiveness by reducing idle times
Previous Example Model 33%
After improving machine process
0.76 0.86 X 0.933= 0.609 61%
After eliminating defects
0.76 0.86 X 1= 0.653 65%
One station can now make 2X as many parts per day in the same 8-hour day

## Slide 19: Improvement Goals for the 6 Big Losses
Type of Loss | Goal | Explanation
1. Breakdowns | 0 | Should be zero for all equipment
2. Setups and adjustments | minimize | As short as possible; less than 10 mins with zero adjustments
3. Reduced speed | 0 | Should match or – with improvements – exceed equipment specifications
4. Minor stoppages | 0 | Should be zero for all equipment
5. Defects and rework | 0 | Extent may vary, but goal should be expressed in parts per million (ppm)
6. Startup loss | minimize | 
Equipment Loss Analysis & OEE
Source: TPM for Every Operator, Productivity Press Development Team

## Slide 20: Setup & Adjustment Losses
Caused by changes in operating conditions, e.g. beginning of production runs or start-up at each shift, changes in products and conditions of operation
These losses consist of setup (equipment changeovers, exchanges of dies, jig and tools), start-up, and adjustment
Magnitude is measured in downtime
Availability

## Slide 21: Minor Stoppage Losses
Caused by events such as machine halting, jamming, idling, misfeeds, blocked sensors, etc.
Generally, these losses cannot be recorded automatically without suitable instruments
Formula: Losses = 100% - Performance Rate
Many companies regard such minor stoppages as breakdowns in order to emphasize their importance, even though no damage has occurred to the equipment
Performance

## Slide 22: Quality Defect & Rework Losses
Caused by off-specification or defective products
  Rework
  Scrap
Losses consist of labor required to rework the products and the cost of the material to be scrapped
Measured by the ratio of quality products to total production
Sometimes designated as “quality defects in process” in order to distinguish from defective products during start-up and adjustment operations
Quality

## Slide 23: Start-up (Yield) Losses
Caused by unused or wasted raw materials
Exemplified by quantity of rejects, scraps, chips, etc.
Yield losses are divided into two groups
  Raw material losses resulting from product designs, manufacturing methods and equipment restrictions
  Adjustment losses resulting from quality defects associated with commencement of work, changeover, etc. Includes setup and adjustment losses plus yield losses, in terms of both time and material losses
Quality

## Slide 24: Strategies for Zero Breakdowns
Restore equipment
Maintain basic equipment conditions
Adhere to standard operating procedures
Improve operator maintenance skills
Don’t stop at quick fixes
Correct design weaknesses
Study breakdowns relentlessly
Equipment Loss Analysis & OEE

## Slide 25
CONTACT INFORMATION:
Eric Ciampoli
President ECIC Consulting Inc.
Cell:917-703-6079 eric@ecicconsulting.com www.ecicconsulting.com