## Slide 1
$Million Minimum Wage Increase Challenge
How One Manufacturer is Cutting Costs
to Stay in NY
Presented by:
Ron Loveland
President
Summit Safety & Efficiency Solutions
www.SummitSafetyPro.com

## Slide 2: Summit Intro
Industrial Engineering Consultants helping manufacturers/industrial customers thrive in Metro NY by improving:
  Safety
  Quality
  Efficiency

## Slide 3: Manufacturer’s Challenge Case Study
Minimum Wage is Rising from $9 to $15 in NYC by 2018
550 employees x $1.75-$2 increase x 2080 hours/year =
>$2m labor cost increase/year!

## Slide 4: Company’s Other Challenges
Market demands: increased sales and shorter lead times
Increased sales growth testing capacity
Large number of small orders require efficient setups
High labor turnover
Productivity issues – weak KPIs to assess
Limited structured problem solving

## Slide 5: Company’s Situation
Low margin, highly competitive market
Labor intensive operations
Space constraints
Seasonal business, 600+ high, 500’s low
83% orders 500 or less
68% orders under 300 pieces

## Slide 6: Opportunities
$1M Annual Expedite (Air Ship) Charges
$4M in Scrap
~35% Productivity
Too much WIP
Too many people

## Slide 7: Approach & Methodology
Value Stream Mapping
  Order Entry process
  Manufacturing and detailed machine process steps
Process Observations
  Various production departments
  Order Management
Materials Management & Inventory Analysis
  Cartons usage & procurement strategies – space
  “SLOBS” – SLow moving and OBSolete material
  Manufactured Product – usage & space

## Slide 8
Overall Findings
No KPIs to drive corrective action
Inaccurate capacity planning
Inventory management/accuracy/warehouse management problems
Quality problems – screens – pinholes & registration
Too much/too little inventory on production floor
Only 35% production available time
Production intermittent-
  Waiting QA, materials, setups, screen problems, …

## Slide 9: Changes to Meet $Million Challenge
  Document Best Practices to support training, continuous improvement, and workforce replacement
  Develop training material for staff, both floor and office
  Product Rationalization - Products with low and negative margins analyzed and phased out

## Slide 10: Changes to Meet $Million Challenge Scrap
  Color Coded Barrels placed at each print station increased visibility and accountability of scrap
  Daily reporting by machine increased visibility & accountability (Hawthorne Effect)

## Slide 11: Warehouse
  Complete warehouse reorganization including location and count accuracy in a timely manner
  Reduce transaction load on warehouse where possible
  Warehouse issues should be full cartons– only count exact quantities when returning to warehouse
  The staging area should be analyzed and organized to reduce extra handling and maximize use of space
  Consolidate picks for like materials rather than per order

## Slide 12: Where’s the Waste?

## Slide 13: Opportunities to Meet $Million Challenge
  The sum of the NVA activities identified totalled 53% available time
  Reducing NVA activities across the production floor by only 10% to 15% could improve annual yield between
  $760k to $1.1mm
  + $1m Scrap Savings
  +$1m Expedite Shipping Savings

## Slide 14: Savings Measures
  Technical issues
    Set up done while other machine operating (cell)
    Screen alignment tools, improved screens
  Non-technical Issues
    Dedicated Quality person to speed sign off
    Eliminate Counting by production personnel
    Reduced Material handling delays/Warehouse improvements
    Color coded barrels at each machine for scrap-Visual Factory
    Product Rationalization

## Slide 15: 1st Year Savings Results
  Eliminated:
  $1m in Expedite charges
  $2m in Scrap
  125 fewer people=$2.86m

## Slide 16: Other Savings Strategies
  Industrial Development Agency Tax Abatement
  Industrial Commercial Abatement Program
  R&D Tax Credit
  Solar Energy
  Workers Compensation Insurance Reduction
  NYC/NYS/Federal Grant & Tax Saving Programs

## Slide 17: Summary
  Minimum wage increase presents major challenge for most NY manufacturers
  Improvements in Productivity, Quality and Inventory Management can help meet that challenge
  The key is improving your processes and involving employees at all levels to sustain improvements
  Constantly improve your processes by identifying and eliminating wasteful activity in the processes

## Slide 18
Improve Business Performance Strategically
Ron Loveland
President
Summit Business Solutions
www.SummitSafetyPro.com
631-642-7239
ron.loveland@lovelandsolutions.com
Questions?
Thank You